## Slide 1: ARM Pipeline
Alireza Bolourian
CPE 300L

## Slide 2
Goal
Build a five-stage pipeline for a subset of the ARMv4 instruction set architecture that supports the standard instructions:
  ADD
  SUB
  ORR
  AND
  LDR
  STR
  B

## Slide 3
Pipeline Diagram
Registers added to divide the processor into 5 stages
Control signals are carried to the next stage by the registers
Hazards need to be addressed
  Data Hazards
  Control Hazards
Digital Design and Computer Architecture ARM Edition by Sarah & David Harris

## Slide 4
RAW Hazard
Hazard created when one instruction writes into a register, and the next instruction reads this register
Solved by forwarding
  Adding multiplexers to the execute stage
  Select operand from Register file, Memory or Writeback stage
  No need to forward from Writeback stage to the Decode stage because it is possible to write and read in the same cycle

## Slide 5
LDR Hazard
LDR does not finish reading until the end of memory stage
It cannot be forward from memory stage
  Stall the Fetch and Decode stages
  Flush the Execute stage

## Slide 6
Control Hazard
Branch decision cannot be made before the next instruction is fetched
Branch prediction
  Branch decision made in execute stage
  Branch multiplexer before the PC register
  Flush Decode and Execute stages

## Slide 7
Simulation Results

## Slide 8
Future Steps
More advanced optimization techniques to reduce the overhead associated with pipelining
  Branch detection in the decode stage
Adding support for parallelism
Implementation on FPGA
Time analysis

## Slide 9
Conclusions
Insight into pipelining and tradeoffs
Hardware simulation and debugging using systemVerilog
Attention to detail and iterative testing

## Slide 10
Questions
Thank You!

## Slide 11
References
Harris, S., & Harris, D. (2015). Digital Design and Computer Architecture. Morgan Kaufmann